SECRET//NOFORN
Raw TCP/UDP Trigger
Hive 2.5
Hive 2.5 Algorithm
400 Bytes
8
0
92
1-byte
XOR
value
Encoded
12-byte
Trigger
8-bytes
Random
Data
CRC
Random
Data
Random Data of length
CRC % 200
12-byte
PAD
Integer
N x 127
25-byte
PAD
2-byte
PAD
CRC
Random Data
The twelve byte trigger is encoded by XORing the 1-byte XOR value with the first five bytes of the trigger and the remaining trigger bytes or XORed with 0xB6.
SECRET//NOFORN

---
SECRET//NOFORN
Raw TCP/UDP Trigger
Hive 2.6
124 Bytes Minimum / 468 Bytes Maximum
0
8
92
0 – 199 Bytes
2 Bytes
2 Bytes
8 Bytes
12 Bytes
8 Bytes
0 – 145 Bytes
START
PAD
8 bytes
CRC
Random
Data
Random Data of length
CRC % 200
Random Data of length
CRC % 146
CRC
PAD1
PAD2
The twelve byte trigger is encoded by computing an offset of CRC % 72 into the CRC random data field and XORing each of the twelve following bytes
with the corresponding byte of the twelve-byte trigger payload.
0
1
2
3
4
5
6
7
8
9
10
11
XOR
key
Connect-back
IP address
Port
Number
Random Data
CRC
SECRET//NOFORN
Integer
N x 127
Encoded
12-byte
Trigger